## Slide 1: Videosondes
Sean Waugh
Specifications:
Dual Instrument System:
HD Camera
PARSIVEL Laser Distrometer
~5.5lbs total weight
HD Camera System:
Model HDC-SD9P
1920x1080 Resolution
1/8000 shutter speed
24 fps
Equivalent sample of 0.3% of each
second
Of Detected Particles, can provide:
Effective radius
Eccentricity
Thermodynamic profile of particle regions (with radiosonde)
Particle Type (i.e. rain, snow, graupel, etc.)
Crystal Habit (plates, columns, aggregates, etc.)
HD Video Camera
Particle Direction
PARSIVEL
LED Batteries/Lights
Specifications:
780 nm Laser
10 sec data interval
Available data:
  Particle Count
  DSD
  Velocity Distribution
Right: Condensed PARSIVEL-2 unit. Data stored locally on micro SD card. Approximately 6 hr battery life.
6.73 mm
6.33 mm
5.8 mm
4.3 mm
PARSIVEL 2 Laser Distrometer
Above: Unmodified PARSIVEL 2 laser distrometer
PArticle Size, Image, and Velocity (PASIV) Probe
Validate sizing accuracy of Camera and Parsivel
Test Objects over diameter range:
Acrylic Ball Bearing -> “Rain-like”
Delrin Ball Bearing -> “Graupel-like”
Can use relationship to
correct measured PSD
4.76 mm Diameter Acrylic
3 mm Diameter Delrin
Raw Image
Imager Analysis
Raw Image
Imager Analysis
Adapting work of Liu et al., 2013 to PASIV
Prob. of Detection =
Height – Height of viewing area in m Numerator = Residence Time
D – Diameter in m Denominator = Sample Time
Velocity – relative particle velocity in m/s
Frame Rate – camera frame rate
If velocity of particle known can correct sampled PSD
List of Operation days | 
Location | Storm Type
May 29th, 2012 – C. OK | Supercell
June 21st, 2012 – C. OK | Multicell
August 15th, 2013 - FL | Weak single cell
August 16th, 2013 - FL | Stratiform
Nov 24th, 2013 – C. OK | Winter Storm
Jul 25th, 2013 – FL | Single cell
August 8th, 2014 – FL | Convective Line
Above: Video segments from indicated operation days.
June 21st, 2012 analyzed PSD sounding with overlaid electric field profile. Comparison indicates correlations between electric field strength and sign with particle distributions.
Conclusions:
Left: PASIV balloon launch on August 1, 2013 in FL during DARPA project.
One-of-a-kind instrument
In-house design
Hybrid system for increased confidence and accuracy
Capable of in situ particle data in under sampled locations of severe weather
  Several Applications
  Storm Electrification (when paired with Electric Field data)
  Dual-Pol Radar validation
  Cloud microphysical research
Rain
Aggregate